## Slide 1
F
Aero Diffusion
Technical Specifications
IconoScent®

## Slide 2
Table of Contents
Aero Diffusion
Technical Specifications 2014
2
Introduction p.3
Technology p.5
Precautions p.6
General Maintenance p.7
Programming p.8
Specifications p.13

## Slide 3
Introduction
3
Aero Diffusion Technology® can be applied by 3 different devices that cover every need. The devices have been designed in order to respond to the demands of any project or area. They are fully programmed and ergonomical.
Aero Diffusion
Technical Specifications 2014

## Slide 4
IconoScent® is a unique solution for distinctive installation on the area. It can be placed on the floor or on a shelf and with it’s fully programmed function to respond to every need
IconoScent®
4
Product Catalogue_02.2014

## Slide 5
Aero Diffusion appliances of Spring Air thanks to the patented diffusion system that they use, they can ensure the conversion of the liquid fragrance into ultra fine droplets ,distributing them at an average of 1.000 nanometers (1 micrometer μm) in diameter.
What can be characterized as being unique concerning the Aero Diffusion Technology® is the small droplet diameter and the extra light weight of the droplet that can ensure uniform scent distribution.
In performance terms, Aero technology droplets convert liquid into vapor very fast. This ensures the absence of residues on surfaces within the scented area. Very important parameter is that the scent effect, which is created, cause very low concentration of fragrance in the air, usually less than 1PPM which is below the international standards for allergic response.
The perfect diffusion of the fragrance into the area can be achieved with the complete programming of the devices. Each device can be programmed for every day separately into two different zones. Thus, given that capability, the aromatization of each space is feasible.
Technology
5
Aero Diffusion
Technical Specifications 2014

## Slide 6
The appliance must be operated in an upright or vertical position and firmly attached to a vertical surface such as a wall or a duct.
The appliance should NOT be used with the door in the open position. The door is opened only to perform a cartridge or program change.
NEVER put your nose to the output of IconoScent®. Within 12 inches of the output, the fragrance is highly concentrated. The improper inhalation of high concentrations of fragrance may cause irritation in eyes and respiratory.
The appliance is built to be plugged into an 110VAC or 220VAC power outlet. The UL and CE compliant power supply converts power to 12V DC to power the appliance.
Unplug before cleaning
IconoScent® Appliance Precautions
6
Aero Diffusion
Technical Specifications 2014

## Slide 7
Changing the Cartridge
Unlock and open the door to access the cartridge: The door should be opened only to perform a cartridge or programming change. When in use, the doom must be locked.
Detach metal hose connector from the cartridge output port (located on the top of the cartridge head). This is done by unscrewing the metal connector from the cartridge output port and pulling out.
Remove air nozzle (located on the top of the cartridge head)
Remove old cartridge from appliance enclosure
Insert air nozzle on the new cartridge
Install new cartridge, place and tighten metal hose connector firmly on cartridge output port
Close the door and the device to secure
General Maintenance
7
Aero Diffusion
Technical Specifications 2014

## Slide 8
We press CLOCK and the indication HOUR is displayed. Using the + button we set HOUR
Programming
8
Day & Time programming
2) We press and the indication MINUTES is displayed. Using the + button we set MINUTES
3) We press . The days of the week will be shown on the screen. Using the + button we move the cursor to the current day
4) We press SET and the day & time programming has been completed
Aero Diffusion
Technical Specifications 2014

## Slide 9
We press 24/7 for 3 seconds and the indication 00 is flashing in the right part of the screen
9
24-hour programming
2) Using the + button we choose one of the 49 intensity options that device programming can give us
3) We press SET and the 24-hour programming has been completed
Note: The device has 49 pre-installed programs in which the fragrance intensity can be adjusted. For example , in program 01 the intensity of the fragrance is the lowest and in the program 49 is the highest
Aero Diffusion
Technical Specifications 2014
Programming

## Slide 10
We press PR button for 3 seconds and we have the days of the week on the screen. Using the + button we move the cursor among the days and with the button we underline the days that we want to function
10
Daily customized programming
We press SET and the indication is ON1 for the chosen days from step 1. Using the + button we adjust the time in which we want the device to start operating and we press
Using the + button we adjust the minutes of the starting working hour of the device
3) We press SET and the indication is OFF1 for the chosen days from step 1. Using the + button we adjust the time in which we want the device to stop operating and we press
Using the + button we adjust the minutes of the ending working hour of the device
(Continue on page 11)
Aero Diffusion
Technical Specifications 2014
Programming

## Slide 11
11
(Continue from page 10)
4) We press SET and the indication 00 is flashing in the right part of the screen for the days we have chosen. Using the + button we choose one of the 49 installed programs (intervals) of the fragrances intensity
5) We press SET and we have the remaining days on screen that need programming. Using the + button we move the cursor under these days and with the button we underline the days that we want to adjust
6) We repeat STEPS 2,3, 4 and 5 until to complete all the days of the week
a) Note in the step 4 of the programming: After the adjustment of the Interval if we choose SET and at the same time button instead of SET only, we have the indication ON2 for the chosen days. Repeating steps 2,3 and 4 we can program a second function zone for the chosen days
Daily customized programming
b) In case we want for day the device to be OFF ex. Sunday we program the Internal 1 00 for that specific day.
Aero Diffusion
Technical Specifications 2014
Programming

## Slide 12
We press CLOCK and the indication HOUR is displayed. Using the + button we set HOUR
12
STEPS
2) We press and the indication MINUTES is displayed. Using the + button we set MINUTES
3) We press . The days of the week will be shown on the screen. Using the + button we move the cursor to the current day
4) We press SET and the day & time programming has been completed
Aero Diffusion
Technical Specifications 2014
Programming

## Slide 13
13
IconoScent®
Technical Characteristics
Reference IconoScent®
Type Cold Evaporation Diffusion device
Diameter of particles 300nm to 1μ micron
Power Input
Input 100 - 240 VAC at 0.6 A
Frequency 50/60 Hz
Protection Switching power supply
Internal Power 12 VDC at 1.5 A
Back-up battery Lithium 3V, #CR2032
Performance Up to 500 m² subject to air flow conditions
Control Programmable start & stop times
Programmable output 1 to 49
Dimensions
Height x width x depth 28cm x 28cm x 13cm
Weight with full container 4,800 kgs
Cartridge
Reservoir 500ml
Disposable/Recyclable
Patented Spring Air
Aero Diffusion
Technical Specifications 2014
Specifications

## Slide 14
Revolutionary solutions
for different
needs…